## Slide 1: Heuristic Two-level Logic Optimization
Giovanni De Micheli
Integrated Systems Laboratory
This presentation can be used for non-commercial purposes as long as this note and the copyright footers are not removed
© Giovanni De Micheli – All rights reserved

## Slide 2: Module 1
Objective
  Data structures for logic optimization
  Data representation and encoding

## Slide 3: Some more background
Function f ( x1, x2, …., xi, …., xn)
Cofactor of f with respect to variable xi
  fxi = f ( x1, x2, …., 1, …., xn)
Cofactor of f with respect to variable xi’
  fxi’ = f ( x1, x2, …., 0, …., xn)
Boole’s expansion theorem:
  f ( x1, x2, …., xi, …., xn) = xi fxi + xi’ fx’i
  Also credited to Claude Shannon
Notes: Given a function f , the co-factors are defined.
Boole’s (or Shannon’s) expansion theorem is defined on the basis of the co-factors.

## Slide 4: Example
Function: f = ab + bc + ac
Cofactors:
  fa = b + c
  fa’ = bc
Expansion:
  f = a fa + a’fa’ = a(b + c) + a’bc
Notes: This simple example shows the computation of cofactors and the expansion of f.

## Slide 5: Unateness
Function f ( x1, x2, …., xi, …., xn)
Positive unate in xi when:
  fxi ≥ fxi’
Negative unate in xi when:
  fxi ≤ fxi’
A function is positive/negative unate when positive/negative unate in all its variables
Notes: A function may be positive (or negative) unate in one or more variables.
If it is not unate, it is called binate.
Unateness is related to monotonicity of the function.
CMOS static gate implement negative unate functions: when an input raises, the output either stays stable or goes down to 0.

## Slide 6: Operators
Function f ( x1, x2, …., xi, …., xn)
Boolean difference of f w.r.t. variable xi:
  ∂f/∂xi ≡ fxi  fxi’
Consensus of f w.r.t. variable xi:
  Cxi ≡ fxi . fxi’
Smoothing of f w.r.t. variable xi:
  Sxi ≡ fxi + fxi’
Notes: Three operators are important in Boolean algebra:
Boolean difference, consensus (universal quantifier) and smoothing (existential quantifier).
The Boolean difference w.r.t. x indicates whether f is sensitive to changes in input x..
When it is zero, then the function does not depend on x.
The concept of Boolean derivative is important in testing. Indeed, any test applied to x must produce effects observable at the circuit outputs to be useful.
The consensus of a function with respect to a variable represents the component that is independent of that variable.
The smoothing of a function with respect to a variable corresponds to dropping that variable from further consideration. Informally, it corresponds to deleting all appearances of that variable.

## Slide 7: Example f = ab + bc + ac
The Boolean difference ∂f/∂a = fa  fa’ = b’c + bc’
The consensus Ca = fa . fa’ = bc
The smoothing Sa ≡ fa + fa’ = b + c
b
a
c
Notes: Examples of Boolean difference, consensus and smoothing.

## Slide 8: Generalized expansion
Given:
  A Boolean function f.
  Orthonormal set of functions:
    i, i = 1, 2, … , k
Then:
  f = ∑ik i  fi
  Where fi is a generalized cofactor.
The generalized cofactor is not unique, but satisfies:
  f  i  fi  f + i’
Notes: It is important to notice that Boole's expansion is a special case of an expansion using an orthonormal basis.
The generalized cofactor may not be unique and satisfies the following bounds listed above.

## Slide 9: Example
Function: f = ab + bc + ac
Basis: 1 = ab and 2 = a’ + b’.
Bounds:
  ab  f1  1
  a’bc + ab’c  f2  ab + bc + ac
Cofactors: f1 = 1 and f2 = a’bc + ab’c.
  f = 1f1 + 2f2
  = ab1 + (a’ + b’)(a’bc + ab’c)
  = ab + bc + ac
Notes: Example of generalized cofactor and expansion.

## Slide 10: Generalized expansion theorem
Given:
  Two function f and g.
  Orthonormal set of functions: i , i=1,2,…,k
  Boolean operator ⊙
Then:
  f ⊙ g = ∑ik i  (fi ⊙ gi)
Corollary:
  f ⊙ g = xi  (fxi ⊙ gxi) + xi’  (fxi’ ⊙ gxi’)
Notes: This theorem states that operations applied to two functions can be reconduced to operations applied to its cofactors.
This gives an important way of solving a problem using recursive structures.
A corollary of this theorem shows that Boolean variables can be used as basis for decomposition as well as for computation.

## Slide 11: Matrix representation of logic covers
Representations used by logic minimizers
Different formats
  Usually one row per implicant
Symbols:
  0, 1, * , …
Encoding:
Notes: Logic covers can be represented by matrices. Usually, these covers use the symbols {0,1,*}.
It is convenient to encode these three symbols by Boolean variables, so that Boolean operations can be applied to rows (or columns) of the matrices.
The positional cube notation is a 2-bit encoding of each symbol.

## Slide 12: Advantages of positional cube notation
Use binary values:
  Two bits per symbols
  More efficient than a byte (char)
Binary operations are applicable
  Intersection – bitwise AND
  Supercube – bitwise OR
Binary operations are very fast and can be parallelized
Notes: With the positional cube notation, a logic representation takes a smaller memory size and operations can be faster.
Two operations are important:
The AND of two rows, which is their intersection, i.e., the largest Boolean subspace contained in both.
The OR of two rows, which is their supercube, i.e., the smallest Boolean subspace containing both.
Note that the supercube is not the union.

## Slide 13: Example
f = a’d’ + a’b + ab’ + ac’d
Notes: Example of positional cube notation.
The first row corresponds to a’d’.
Thus, the first field is a 0 for a, i.e., encoded by 10.
The fourth field is a a 0 for d, also encoded by 10.
The second and third fields are don’t cares on b and c, encoded by 11.

## Slide 14: Cofactor computation
Cofactor of α w.r. to β
  Void when α does not intersect β
  a1 + b1’ a2 + b2’ … an + bn’
Cofactor of a set C = {γi} w.r. to β:
  Set of cofactors of γi w.r. to β
Notes: The cofactor is computed by the following procedure when using matrices.
Its computation is fast and efficient.

## Slide 15: Example f = a’b’ + ab
Cofactor w.r. to 01 11
  First row – void
  Second row – 11 01
Cofactor fa = b
10 10
01 01
01 11
10 10
00 10
void
01 01
01 01
10 00
11 01
Notes: Example of cofactor computation.

## Slide 16: Multiple-valued-input functions
Input variables can take many values
Representations:
  Literals: set of valid values
  Function = sum of products of literals
Positional cube notation can be easily extended to mvi
Key fact
  Multiple-output binary-valued functions represented as mvi single-output functions
Notes: A multiple-valued function is a function whose input and output variables can take two or more values.
Multiple-valued functions and their optimization have been studied for several reasons, originally to provide support for designing logic circuits with more than two logic values, such as three and four-valued PLAs and ROMs.
Recently, techniques for manipulating multiple-valued logic functions have been used to design binary-valued circuits, that implement some encoding of the multiple-values.
Mvi-functions can be represented in different ways, including sop and pos of literals.
A literal is true when the variable takes a value in the corresponding set; otherwise it is false.
The concepts of minterm, implicant, prime and essential can be extended in a straightforward way.
When considering any multiple-output function, it is always possible to represent it as the corresponding single-output characteristic function.
In particular, when considering a multiple-output binary-valued function, it is possible to interpret the output-part of its implicants (with m bits) as an encoding of a m--valued input of a corresponding mvi representation.

## Slide 17: Example
2-input, 3-output function:
  f1 = a’b’ + ab
  f2 = ab
  f3 = ab’ + a’b
Mvi representation:
Notes: This example shows that a 2-input, 3-output function can be represented by three fields, the third representing the output field.
This can be seen as a 3-input, 1-output function, where the third field is a 3-valued input.

## Slide 18: Module 2
Objective
  Operations on logic covers
  Application of the recursive paradigm
  Fundamental mechanisms used inside minimizers

## Slide 19: Operations on logic covers
Recursive paradigm
  Expand about a mv-variable
  Apply operation to co-factors
  Merge results
Unate heuristics
  Operations on unate functions are simpler
  Select variables so that cofactors become unate functions
Recursive paradigm is general and applicable to different data structures
  Matrices and binary decision diagrams
Notes: The recursive paradigm for operating on lists of implicants exploits a corollary of the orthonormal expansion Theorem.
The meaning of this corollary is that an operation on a set of implicants can be done on a variable by variable basis.
An operation can be carried out by merging the results of the operation applied to the cofactors with respect to a chosen variable.
Thus operations on sets of implicants can be computed recursively.
At every level of the recursion a simpler problem needs to be solved.
Whereas the recursive approach to handling logic functions has been known for long time, it was not until recently that its full power was exploited.
The key lies in the fact that operations on unate functions are simpler to be solved.
While most logic functions are not unate, the recursive decomposition may lead to cofactors that are unate, and whose processing is very efficient.
The so called unate recursive paradigm consists of exploiting the properties of unate functions within a recursive expansion.

## Slide 20: Tautology
Check if a function is always TRUE
Recursive paradigm:
  Expend about a mvi variable
  If all cofactors are TRUE, then the function is a tautology
Unate heuristics
  If cofactors are unate functions, additional criteria to determine tautology
  Faster decision
Notes: Tautology plays an important role in all algorithms for logic optimization.
Despite the intractability of the problem, the question if a function is a tautology can be answered efficiently using the recursive paradigm.
For binary-valued functions, a function f is a tautology if and only if its cofactors with respect to any variable and its complement are both a tautology.
For mvi-functions, a function f is a tautology if and only if all its generalized cofactors with respect to the values of any variable are a tautology.
Therefore, the tautology question can be answered by expanding a function about a variable, and checking recursively whether its cofactors are a tautology.
The unate heuristics speeds up the computation.

## Slide 21: Recursive tautology
TAUTOLOGY:
  The cover matrix has a row of all 1s. (Tautology cube)
NO TAUTOLOGY:
  The cover has a column of 0s. (A variable never takes a value)
TAUTOLOGY:
  The cover depends on one variable, and there is no column of 0s in that field
Decomposition rule:
  When a cover is the union of two subcovers that depend on disjoint sets of variables, then check tautology in both subcovers
Notes: A recursive tautology computation can be terminated by the rules above. For more rules and details, see the textbook.

## Slide 22: Example f = ab + ac + ab’c’ + a’
Select variable a
Cofactor w.r. to a’ is
11 11 11 – Tautology.
Cofactor w.r. to a is:
11 01 11
11 11 01
11 10 10
10 11 11
01 01 11
01 11 01
10 11 11
01 10 10
10 11 11
01 00 00
01 11 11
11 11 11
10 00 00
00 01 11
00 11 01
00 10 10
00 11 11
01 01 11
01 11 01
01 10 10
11 01 11
11 11 01
11 10 10
a
b
c
Notes: This is an animated example of tautology computation.

## Slide 23: Example (2)
11 01 11
00 10 00
Select variable b
Cofactor w.r. to b’ is
No column of 0 - Tautology
Cofactor w.r. to b:
Function is a TAUTOLOGY
11 10 11
11 01 11
11 11 01
11 10 10
00 01 00
11 01 11
11 01 01
11 00 10
11 00 11
11 10 01
11 10 10
11 11 11
11 11 01
11 11 01
11 11 10
11 11 01
11 11 10
Has row of 1s
11 01 11
11 11 01
11 10 10

## Slide 24: Containment
Theorem:
  A cover F contains an implicant α if and only if Fα is a tautology
Consequence:
  Containment can be verified by the tautology algorithm
Notes: The question whether a cover F contains (i.e. covers) an implicant alpha can be reduced to a tautology problem by using the above theorem.
As a result, containment can be solved by the tautology algorithms.

## Slide 25: Example f = ab + ac + a’
Check covering of bc : 11 01 01.
Take the cofactor:
Tautology – bc is contained by f.
a
b
c
01 11 11
01 11 11
10 11 11
Notes: Example of containment

## Slide 26: Complementation
Recursive paradigm
  f’ = x f’x + x’ f’x’
Steps:
  Select variable
  Compute co-factors
  Complement co-factors
Recur until cofactors can be complemented in a straightforward way
Notes: The complementation of a function, implemented by using the unate recursive
paradigm, has shown to be very efficient.
The original algorithm was designed for single-output bv-functions; complementation of multiple-output bv-functions was achieved by repeated invocation of the algorithm for each output.
Therefore the complement of a function f can be computed recursively by using the (complemented)
covers of the cofactors of f.

## Slide 27: Termination rules
The cover F is void
  Hence its complement is the universal cube
The cover F has a row of 1s
  Hence F is a tautology and its complement is void
The cover F consists of one implicant.
  Hence the complement is computed by DeMorgan’s law
All implicants of F depend on a single variable, and there is not a column of 0s.
  The function is a tautology, and its complement is void
Notes: The recursive procedure terminates, or can be simplified, when the cover of F satisfies one of the following conditions.

## Slide 28: Unate functions
Theorem:
  If f is positive unate in x, then
    f’ = f’x + x’ f’x’
  If f is negative unate in x, then
    f’ = x f’x + f’x’
Consequence:
    Complement computation is simpler
    Follow only one branch in the recursion
Heuristics
  Select variables to make the cofactor unate
Notes: The choice of the splitting variable is based upon the unate recursive paradigm.
Indeed, the computation of the complement is simpler for unate functions, as shown by the theorem above.

## Slide 29: Example f = ab + ac + a’
Select binate variable a
Compute cofactors:
  Fa’ is a tautology, hence F’a’ is void.
  Fa yields:
11 01 11
11 11 01
a
b
c
Notes: Example of a complementation.

## Slide 30: Example (2)
Select unate variable b
Compute cofactors:
  Fab is a tautology, hence F’ab is void
  Fab’ = 11 11 01 and its complement is 11 11 10
Re-construct complement:
  11 11 10 intersected with Cube(b’) = 11 10 11 yields 11 10 10
  11 10 10 intersected with Cube(a) = 01 11 11 yields 01 10 10
Complement: F’ = 01 10 10

## Slide 31: Example (3)
Recursive search:
Fa’ = TAUT
COMP = ø
Fab’ = c
COMP = c’
Fab = TAUT
COMP = ø
a’
b
b’
a
Complement: a b’c’

## Slide 32: Boolean cover manipulation summary
Recursive methods are efficient operators for logic covers
  Applicable to matrix-oriented representations
  Applicable to recursive data structures like BDDs
Good implementations of matrix-oriented recursive algorithms are still very competitive
  Heuristics tuned to the matrix representations
Notes: In summary, the recursive unate paradigm is widely used for manipulating logic covers.
Most minimizers use matrix representations, even though the decomposition can also be achieved on other data structures, such as decision diagrams.

## Slide 33: Module 3
Objectives
  Heuristic two-level minimization
  The algorithms of ESPRESSO

## Slide 34: Heuristic logic minimization
Provide irredundant covers with “reasonably small” sizes
Fast and applicable to many functions
  Much faster than exact minimization
Avoid bottlenecks of exact minimization
  Prime generation and storage
  Covering
Motivation
  Use as internal engine within multi-level synthesis tools
Notes: Heuristic logic minimizations strives at computing fast a minimal cover with reasonably small cardinality.
It avoids the bottlenecks of exact minimization, by avoiding the computation of ALL primes and solving a covering problem exactly.

## Slide 35: Heuristic minimization -- principles
Start from initial cover
  Provided by designer or extracted from hardware language model
Modify cover under consideration
  Make it prime and irredundant
  Perturb cover and re-iterate until a small irredundant cover is obtained
Typically the size of the cover decreases
  Operations on limited-size covers are fast
Notes: Heuristic minimization is done by starting from an initial cover and then performing a stepwise refinement.
This refinement can only reduce the size of the cover, thus avoiding any unexpected blow up in size.
Typically, a cover is made prime and minimal. Then it is perturbed, and another prime and minimal cover is obtained. The latter cover is retained if smaller than the previous one.

## Slide 36: Heuristic minimization - operators
Expand
  Make implicants prime
  Removed covered implicants
Reduce
  Reduce size of each implicant while preserving cover
Reshape
  Modify implicant pairs: enlarge one and reduce the other
Irredundant
  Make cover irredundant
Notes: Most heuristic minimizers would use these four operators on logic covers.

## Slide 37: Example
Initial cover
  (without positional cube notation)
Notes: This is an example of logic minimization, as done by minimizer MINI.
This is the starting point.

## Slide 38: Example
Set of all primes
a
b
c
d
α 0 * * 0 1
ζ * 1 0 1 1
ε 1 * 0 1 1
δ 1 0 * * 1
γ 0 1 * * 1
β * 0 * 0 1
0111
1011
0110
0010
0000
0101
1001
1101
0100
1010
1000
Notes: This picture shows all primes. This is for explanation only. The minimizer would not compute ALL primes.

## Slide 39: Example of expansion
Expand 0000 to α = 0**0.
  Drop 0100, 0010, 0110 from the cover.
Expand 1000 to β = *0*0.
  Drop 1010 from the cover.
Expand 0101 to γ = 01**.
  Drop 0111 from the cover.
Expand 1001 to δ = 10**.
  Drop 1011 from the cover.
Expand 1101 to ε = 1*01.
Cover is: {α,β,γ,δ,ε}.
a
b
c
d
1001
0111
1011
0110
0010
0000
0101
1101
0100
1010
1000
Notes: This animation shows the expansion of the implicants and the cover achieved after expansion.

## Slide 40: Example of reduction
Reduce 0**0 to nothing.
Reduce β = *0*0 to β’ = 00*0.
Reduce ε = 1*01 to ε’ = 1101.
Cover is: {β’,γ,δ,ε’}.
a
b
c
d
1001
0111
1011
0110
0010
0000
0101
1101
0100
1010
Notes: This animation shows the reduction of the implicants.

## Slide 41: Example of reshape
Reshape {β’, δ} to: {β, δ’}.
  Where δ’ = 10*1.
Cover is: {β,γ,δ’,ε’}.
a
b
c
d
1001
0111
1011
0110
0010
0000
0101
1101
0100
1010
Notes: This animation shows a reshape.

## Slide 42: Example of second expansion
Expand δ’ = 10*1 to δ = 10**.
Expand ε’ = 1101 to ε = 1*01.
a
b
c
d
1001
0111
1011
0110
0010
0000
0101
1101
0100
1010
Notes: This animation shows a second expansion, leading to the final minimal cover.

## Slide 43: Example Summary of the steps taken by MINI
Expansion:
  Cover: {α,β,γ,δ,ε}.
  Prime, redundant, minimal w.r. to scc.
Reduction:
  α eliminated.
  β = *0*0 reduced to β’ = 00*0.
  ε = 1*01 reduced to ε’ = 1101.
  Cover: {β’,γ,δ,ε’}.
Reshape:
  {β’, δ} reshaped to: {β, δ’} where δ’ = 10*1.
Second expansion:
  Cover: {β,γ,δ,ε}.
  Prime, irredundant.
α
ε
δ
γ
β
0111
1011
0110
0010
0000
0101
1001
1101
0100
1010
0111
1011
0110
0010
0000
0101
1001
1101
0100
1010
Notes: Minimizer MINI does the following.
It computes a prime and minimal (wrt containment) cover via one expansion.
It iterates operators (reduce, reshape and expand) to improve upon this cover.

## Slide 44: Example Summary of the steps taken by ESPRESSO
Expansion:
  Cover: {α,β,γ,δ,ε}.
  Prime, redundant, minimal w.r. to scc.
Irredundant:
  Cover: {β,γ,δ,ε}.
  Prime, irredundant.
a
b
c
d
1001
0111
1011
0110
0010
0000
0101
1101
0100
1010
Notes: Minimizer ESPRESSO takes a faster route.
It computes a prime and irredundant cover via operators expand and irredundant
It iterates operators (reduce, expand, irredundant) to improve on this solution

## Slide 45: Rough comparison of minimizers
MINI
  Iterate EXPAND, REDUCE, RESHAPE
Espresso
  Iterate EXPAND, IRREDUNDANT, REDUCE
Espresso guarantees an irredundant cover
  Because of the irredundant operator
MINI may return irredundant covers, but can guarantee only minimality w.r.to single implicant containment
Notes: Espresso gives results that are guaranteed to be irredundant (i.e. minimal w.r.to containment).
Often Espresso yields a minimum cover.
Due also to speed, Espresso is used within most logic synthesis tools.

## Slide 46: Expand Naïve implementation
For each implicant
  For each care literal
    Raise it to don’t care if possible
  Remove all implicants covered by expanded implicant
Issues
  Validity check of expansion
  Order of expansion
Notes: The expand operator is used by most heuristic minimizers.
Its goal is to increase the size of each implicant of a given cover F, so that implicants of smaller size can be covered and deleted.
Maximally expanded implicants are primes of the function.
As a result, the expand operator makes a cover prime and minimal with respect to single implicant containment.
The expansion of an implicant is done by raising one (or more) of its 0s to 1s.
This corresponds to increasing its size (by a factor of two per raise), and therefore to covering more minterms.
The fundamental question in the expansion process is whether the expanded cube is still valid, i.e. it is still an implicant of the function $f$.

## Slide 47: Validity check
Espresso, MINI
  Check intersection of expanded implicant with OFF-set
  Requires complementation
Presto
  Check inclusion of expanded implicant in the union of the ON-set and DC-set
  Reducible to recursive tautology check
Notes: There are two major approaches for the validity test.
- Checking for an intersection of the expanded implicant with the OFFSET.
The intersection can be computed very efficiently, but the OFFSET is required, and sometimes it may overflow the memory size and cause the minimizer to fail.
Nevertheless this is the approach used by most minimizers, such as Mini and Espresso.
- Checking for the covering of the expanded implicant by the union of the ONSET and the DCSET.
In this approach, the OFFSET is not needed.
This method was used by program Presto, where the covering test
was solved recursively.
The containment check can be also reduced to tautology problem.
Espresso uses this strategy in special cases.

## Slide 48: Ordering heuristics
Expand the cubes that are unlikely to be covered by other cubes
Selection:
  Compute vector of column sums
  Weight: inner product of cube and vector
  Sort implicants in ascending order of weight
Rationale:
  Low weight correlates to having few 1s in densely populated columns
Notes: The expand procedure sorts the implicant one at a time and expands the 0 entries to 1, subject to the validity of the expanded implicant. The computational efficiency and the quality of the result depend on two important factors:
(i) the order in which the implicants are selected;
(ii) the order in which the 0 entries are raised to 1.
Heuristic rules are used in both cases.
The rationale is to expand first those cubes that are unlikely to be covered by other cubes.
The technique is the following.
A vector is computed whose entries are the column sums of the matrix representing F.
Each cube is assigned a weight that is the inner product of the cube itself and the previously computed vector.
A low weight of a cube correlates to the cube having few ones in the densely populated columns.
Therefore the implicants are sorted for ascending weights.

## Slide 49: Example
f = a’b’c’ + ab’c’ + a’bc’ + a’b’c
DC-set = abc’
Ordering:
  Vector: [3 1 3 1 3 1]T
  Weights: (9, 7, 7, 7)
Select second implicant.
10 10 10
01 10 10
10 10 01
10 01 10
Notes: Example of sorting the implicants for expansion.

## Slide 50: Example (2)
b
a
c
α 10 10 10
δ 10 10 01
DC 01 01 10
γ 10 01 10
β 01 10 10

## Slide 51: Example (3)
OFF-set:
Expand 01 10 10:
  11 10 10 valid.
  11 11 10 valid.
  11 11 11 invalid.
Update cover to:
01 11 01
11 01 01
11 11 10
10 10 01

## Slide 52: Example (4)
Expand 10 10 01:
  11 10 01 invalid.
  10 11 01 invalid.
  10 10 11 valid.
Expanded cover:
11 11 10
10 10 01
11 11 10
10 10 11

## Slide 53: Expand heuristics in ESPRESSO
Special heuristic to choose the order of literals
Rationale:
  Raise literals so that the expanded implicant
    Covers a maximal set of cubes
    Overlaps with a maximal set of cubes
    The implicant is as large as possible
Intuitive argument
  Pair implicant to be expanded with other implicants, to check the fruitful directions for expansion
Notes: The heuristics for selecting the entries to expand are complex.
Many different primes can be derived by expanding the cube in different directions.
Each prime may cover different subsets of F.
The major goal is to cover the largest subset of implicants of F.
In Espresso, the goal is to make the implicant prime, while covering a maximal number of other implicants. A quick analysis of the position of the implicant in the Boolean space with respect to the offset allows us to determine some feasible and unfeasible directions for expansion, but not all.
Thus, the next step is to search for other cubes in the cover, that would be covered by a specific feasible expansion.
When this search is exhausted, we look for expansion directions that allow the expanded implicant to overlap a maximal number of other cubes.
In the end, we just make the implicant prime by making it as large as possible.

## Slide 54: Expand in Espresso
Compare implicant with OFF-set.
  Determine possible and impossible directions of expansion
Detection of feasibly covered implicants
  If there is an implicant β whose supercube with α is feasible, expand α to that supercube and remove β
Raise those literals of α to overlap a maximum number of implicants
  It is likely that the uncovered part of those implicant is covered by some other expanded cube
Find the largest prime implicant
  Formulate a covering problem and solve it heuristically
Notes: The description of the expand steps in Espresso is detailed in the textbook.

## Slide 55: Reduce
Sort implicants
  Heuristics: sort by descending weight
  Opposite to the heurstic sorting for expand
Maximal reduction can be determined exactly
Theorem:
  Let α be in F and Q = F U D – { α } Then, the maximally reduced cube is: ά = α ∩ supercube (Q’α)
Notes: The reduce operator is used by most heuristic minimizers.
Its goal is to decrease the size of each implicant of a given cover F, so that a successive expansion may lead to another cover of smaller cardinality.
A reduced implicant is valid when, along with the remaining implicants,
still covers the function.
The reduced implicant can be determined in a unique way by means of a theorem.
The reduced cover has the same cardinality as the original one.
Reduced covers are not prime (unless no implicant can be reduced.)
Note that a redundant implicant would be reduced to a void one, that can be discarded, if reduced before the implicants that cover it.

## Slide 56: Example
Expand cover:
Select first implicant:
  Cannot be reduced.
Select second implicant:
  Reduced to 10 10 01
Reduced cover:
11 11 10
10 10 11
11 11 10
10 10 01
Notes: Example of reduction

## Slide 57: Irredundant cover
b
a
c
α 10 10 11
δ 01 01 11
γ 01 11 01
β 11 10 01
ε 11 01 10
Notes: To motivate the algorithm for finding an irredundant cover, just observe the cover in the picture.
There are 5 primes.
Note that the ste of ALL primes has cardinality 6.
There is an irredundant cover or 3 primes and one of 4 primes.
Thus, our objective is to find an irredundant cover with a minimal number of primes.
Note that we are not looking for a minimum number of primes for 3 reasons:
This is not exact minimization
The search for a minimum would involve solving an intractable problem.
Even if we solve the problem exactly, we may miss the minimum cover because not all primes are available,

## Slide 58: Irredundant cover
Relatively essential set Er
  Implicants covering some minterms of the function not covered by other implicants
  Important remark: we do not know all the primes!
Totally redundant set Rt
  Implicants covered by the relatively essentials
Partially redundant set Rp
  Remaining implicants
Notes: The cover F is split first into three sets:
-The relatively essential set that contains those implicants that cover some minterms of the function not covered by other implicants of F
-The totally redundant set that contains those implicants that are covered by the relatively essential set.
-The partially redundant set that contains the remaining implicants.

## Slide 59: Irredundant cover
Find a subset of Rp that, together with Er covers the function
Modification of the tautology algorithm
  Each cube in Rp is covered by other cubes
  Find mutual covering relations
Reduces to a covering problem
  Apply a heuristic algorithm.
  Note that even by applying an exact algorithm, a minimum solution may not be found, because we do not have all primes.
Notes: An irredundant cover is the union of the partially redundant set with the relative essential set.
The algorithm for computing the partially redundant primes uses a modification of the tautology check.
The key idea is the following.
Rather than checking the tautology, we determine the set of cubes that, when removed, prevents the function from being a tautology.
Recall that tautology of the cofactor can be used to determine containment.
Hence we can determine the set of cubes that, when removed, prevent the containment.
When the tautology algorithm reaches a leaf, we mark the corresponding cubes that cause the tautology.
If a leaf is related to any cube in the essential set, we drop the leaf from consideration.
Otherwise, we mark the cubes that come from the relative essential set.

## Slide 60: Example
Er = {α, ε}
Rt = ∅
Rp = {β, γ, δ}
α 10 10 11
δ 01 01 11
γ 01 11 01
β 11 10 01
ε 11 01 10
Notes: Example. 5 primes, 2 of which are relatively essential.
The mutual covering relations among the remaining 3 primes are determined.

## Slide 61: Example (2)
Covering relations:
  β is covered by {α, γ}.
  γ is covered by {β, δ}.
  δ is covered by {γ, ε}.
Minimum cover: γ U Er
Notes: This picture shows the mutual covering relations, as well as the selection of a minimal set of partially redundant primes.

## Slide 62: ESPRESSO algorithm in short
Compute the complement
Extract essentials
Iterate
  Expand, irredundant and reduce
Cost functions:
  Cover cardinality φ1
  Weighted sum of cube and literal count φ2
Notes: Espresso is a very fast and efficient two-level minimizer.
It exploits the operators described above, while performing an iterative refinement of a cover.
The output of Espresso is an irredundant cover, often minimum in cardinality.

## Slide 63: ESPRESSO algorithm in detail
  espresso(F,D) {
    R = complement(F U D);
    F = expand(F,R);
    F = irredundant(F,D);
    E = essentials(F,D);
    F = F – E; D = D U E;
    repeat {
      2 = cost(F);
      repeat {
        1 = |F |;
        F = reduce(F,D);
        F = expand(F,R);
        F = irredundant(F,D);
      } until (|F | ≥ 1);
      F = last_gasp(F,D,R);
    } until (cost( F ) ≥ 2);
    F = F U E; D = D – E;
    F = make_sparse(F,D,R);
  }
Notes: Espresso computes first the complement of a cover to be used by the expand operator.
Then it applies the expand and irredundant operators, that make the cover prime and irredundant.
After the essentials are extracted, Espresso iterates the reduce, expand and irredundant operators in the search for irredundant covers of decreasing cardinalities.
When no improvement can be achieved, then Espresso attempts to reduce and expand the cover using a different heuristic.
Eventually Espresso applies the routine make_spars}, that modifies the numbers of 1/0s in the array without affecting the cardinality of the cover.

## Slide 64: ESPRESSO algorithm in detail
  espresso(F,D) {
    R = complement(F U D);
    F = expand(F,R);
    F = irredundant(F,D);
    E = essentials(F,D);
    F = F – E; D = D U E;
    repeat {
      2 = cost(F);
      repeat {
        1 = |F |;
        F = reduce(F,D);
        F = expand(F,R);
        F = irredundant(F,D);
      } until (|F | ≥ 1);
      F = last_gasp(F,D,R);
    } until (cost( F ) ≥ 2);
    F = F U E; D = D – E;
    F = make_sparse(F,D,R);
  }
Notes: Espresso computes first the complement of a cover to be used by the expand operator.
Then it applies the expand and irredundant operators, that make the cover prime and irredundant.
After the essentials are extracted, Espresso iterates the reduce, expand and irredundant operators in the search for irredundant covers of decreasing cardinalities.
When no improvement can be achieved, then Espresso attempts to reduce and expand the cover using a different heuristic.
Eventually Espresso applies the routine make_spars}, that modifies the numbers of 1/0s in the array without affecting the cardinality of the cover.

## Slide 65: Heuristic two-level minimization Summary
Heuristic minimization is iterative
Few operators are applied to covers
Underlying mechanism
  Cube operation
  Unate recursive mechanism
Efficient algorithms
Notes: In summary, heuristic minimization uses an iterative paradigm.
There are few operators applied to a cover, and the iteration terminates when the operators cannot reduce the cover further.
The underlying mechanisms are the cube operations and the unate recursive paradigm.